Medical Teaching Institution (MTI)

Lady Reading Hospital (LRH)

Peshawar

Contact No: 091-9211927

INFORMATION DOCUMENTS

For

THE PROCUREMENT OF MEDICAL EQUIPMENTS & OTHER ITEMS

(in Pursuance to the declaration of Emergency vide letter No. SOG/HD/1-102/Gen.Corr./2020, Dated April 1st, 2021 regarding emergency procurements.)

Note: The prospective bidder is expected to examine the Bidding Documents carefully, including all Instructions, Terms & Conditions, and Specifications etc. Failure to furnish all information required by the Bidding documents or submission of a Bid not substantially responsive to the Bidding Documents in every respect would result in the rejection of the Bid.

Terms & Conditions

The envelopes shall be marked as “TECHNICAL BID” and “FINANCIAL BID” and in Bold and Legible letters to avoid confusion. Similarly, the bidder shall seal both bids in separate envelopes. The said two envelopes shall then be sealed in an outer envelope.

- The firm should be registered with Income Tax & Sales Tax Department (Registration Numbers should be clearly mentioned and valid documentary evidence).

- The contract will be awarded to firms having technical compliance with the specifications, delivery time and lowest price. The department reserves the right based on need on COVID-19 to decide on the basis of delivery time &/or Lowest quoted price as the case may be after compliance with specification.

- Submission of false statement / documents as well as concealing of any information is liable to disqualify the respective firm/s.

- The Procuring Entity reserves the right to accept or reject all or any of the tenders as laid down in bid solicitation documents.

- Firm shall submit an affidavit on Stamp Paper that the Firm/Company has never been blacklisted by any Government Ministry/Division/Department.

- Incomplete, conditional and bid/s received after due date and time shall not be entertained.

- Bidders shall provide mandatory warranty for three years with parts and services, and after mandatory warranty two years services without parts.

- Bidders shall clearly mention in quotation the country of origin, model, and product certifications like CE, JIS, USFDA etc. and ISO’s. These mentioned documents shall preferably be submitted with the proposal, if any.

- There is possibility of variation (increase/decrease) in quantity mentioned due to unforeseen situation in Emergency and Donors Commitments based on recommendations of Public health of this directorate.

- The Unit price quoted by the bidder shall be in Pakistani Rupees: inclusive of all duties, taxes & levies as per law.

- The successful bidder/s shall be bound to submit 10% performance security before signing the contract. Non provision of the same shall lead to disqualification of the successful bidder and the purchasing agency shall have the full authority to award contract to the next highest bidder.

- Based on the required number of equipment, multiple contracts can be awarded to fulfill the need of COVID-19

- The sole Agent/Authorized dealer shall have to provide a valid proof of being authorized dealer of the principal manufacturer and/ or submit affidavit for providing services as per agreement.

- In case of failure to comply with contract provision &/or Supply order, the firm shall be processed for blacklisting.

- Lowest Evaluated Responsive Bid shall be the Selection Criteria for this emergency Procurement shall be;

  - Registration of firm with Income Tax & Sales Tax Department

  - Compliance with the specification

  - Mandatory warranty provision

  - Compliance with certification Provision

  - Delivery Timeline as this is Emergency Procurement to Cope with COVID-19 Emergency

  - Lowest Quoted Rates.

- Submit your quotation on the below format

Technical Bid Quotation Form:

| S.No | Name of Equipment | Model & Country of Origin (Make) | Product Certifications and ISO | Compliance with Specifications (Yes/No) | Available Quantity | Delivery Time (in Days) |
| --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |  |

Financial Quotation:

| S.No | Name of Equipment | Model & Country of Origin (Make) | Product Certifications and ISO | Compliance with Specifications (Yes/No) | Available Quantity | Delivery Time (in Days) | Price in (Rs) (inclusive applicable taxes) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |  |  |

TECHNICAL EVALUATION CRITERIA

| S # | PARAMETERS | SUB-PARAMETERS | MARKS |
| --- | --- | --- | --- |
| 1 | Legal / Financial Requirements |  |  |
|  |  | CE/USFDA/MHLW (at least one is mandatory) while For serial No.5,8,9 two of the above certificates are mandatory. | Mandatory |
|  |  | NTN Registration Certificate |  |
|  |  | KNTN Registration Certificate |  |
|  |  | Sales & Professional Tax Certificate |  |
|  |  | Letter of Commitment for delivery period to be mention |  |
| 2 | TECHNICAL STAFF |  | 25 |
|  | Compliance with specifications | Compliance with specifications (yes/No viz-a-viz format) |  |
| 3 | Delivery time |  | 25 |
|  | Product delivery time/period (after issuance of purchase order) | Delivery 30% stock within 15 days Delivery 30% stock within 10 days Delivery 30% stock within 7 days More than 15 days will get 0 marks | 10 15 25 |
|  | Total Marks | 50 |
|  | Qualifying Marks | 35 |

Note: Lowest price will consider for each equipment of technically qualified bidders, technical marks are only for qualifying purpose.  warranty 3 years with parts including accessories and disposables and 2 years without parts is mandatory

Specification & proposed Quantity

| 1 | Electric Cardiac Bed/ICU Bed Quantity = 40 | Motorized, battery operated Cardiac /ICU bed with remote controller The bed model must be CE approved The Bed must facilitate a metal constructed, mattress surface covered with 4-section abs Materials, ABS covered sub-frame. The Sub-frame under the mattress surface must be covered with steel Material. The Bed must have fold- Away ABS side rails on both sides of the bed, controlled separately The bed facilitates a hand control panel which must have adjustments of the following functions a) Backrest up-down b) Footrest up-down c) Bed height up-down The bed must have electrical Trendelenburg and reverse Trendelenburg adjustment. Between +120 by means of hand control unit. Fowler, vascular, cardiac chair position and auto-contour positions by hand control unit. The backrest section of the bed must be able to be adjusted between 0-700 The bed must be equipped with auto-regression system at back rest. The footrest section must be able to be adjusted between 0-350 or better. Central brake system or lockable castors. The bed must facilitate 4 IV pole sockets and head and footboards sockets made a plastic, located under the head and footboards. The bed must facilitate 4 protective bumpers on external corners to prevent damage on the contact area during bed movements and transfer. The bed must work on 220V/ 50 Hz have rechargeable battery backup for movement control. There must be urine bag hangers on both sides of the bed. Battery backup 2 hours Gradually adjustable footrest. The metal parts of the bed must bed epoxy powder quoted. The bed must have a safe load bearing capacity of 230 Kg or more. The bed’s height must be able to be adjusted between 40cm and 70cm. or better There must be manual CPR function Overall width 85 cm or more. Overall length 195cm or more. Side Railing/ side guard The bed should have facility to take X-Ray of the patient over the bed (cassette holder). Accessories: One extra remote with each unit (Mandatory) |
| --- | --- | --- |
| 02 | ICU Ventilator with turbine and humidifier Quantity: 25 | For adult and Paeds Tidal volume 50-2000 ml or better Pressure up to 80 cm H20 Volume up to 120 L/min Respiratory rate: up to 60 breaths per minute. SIMV Respiratory Rate: up to 40 breaths per minute. CPAP/PEEP up to 20 cm H2O. Pressure support up to 45 cm H2O. FiO2 between 21 to 100 % I:E Ratio at least from 1:1 to 1:3. Modes of ventilation: a) Volume controlled. b) Pressure controlled. c) Pressure support. d) Synchronized intermittent mandatory ventilation (SIMV) with pressure support. e) Assist / control mode f) CPAP/PEEP g) PSV h) SPONT i) Active nebulization function Alarms required: FiO2, minute volume, pressure, PEEP, apnea, occlusion, high respiration rate, disconnection Display size: min 10-inch Lcd/Led or better System alarms required: power failure, gas disconnection, low battery, vent inoperative, self-diagnostics Air and externally supplied oxygen mixture ratios fully controllable Inlet gas supply (O2) pressure range at least 35 to 65 psi Integrated medical Turbine system with inlet filter Air hose line with probe O2 hose line with probe Re-usable/ autoclavable patient circuit for adult and paeds With Humidifier (Fisher and Paycal) |
| 03 | BIPAP Quantity: 40 | Pressure range:IPAP 4 - 30 cm H2O; EPAP 4 - 25 cm H2O; CPAP 4 - 20 cm H₂O Modes : CPAP, S, S/T, PC, T Breath rate : 0 - 30 beats per minute Device should have CPAP, BILEVEL S, BILEVEL T, BILEVEL ST modes. Device should have three different user menus – an Information menu, a patient menu for adjusting the comfort functions and a clinical menu for the optimal customization of all the therapy parameters. Once the patient stops breathing the device should automatically switches into the T-mode and provides respiration for the patient in the prescribed safety frequency. The extreme low respiration resistance, the high-powerreserves, and the automatic compensation for leakages. The device should have start-stop-automatic, soft start ramp, leakage test, leakage alarm, power failure alarm, automatic turbine starts after power failure, date, time, and wake-up function. Average noise level should be less than 26 dB. Advanced data management with SD card. Simple handling. Easy to replace filter. |
| 04 | CPAP Quantity: 40 | A.SPECIFICATIONS FOR CONTINUOUS POSITIVE AIRWAY PRESSURE (CPAP) 1. Should be light weight, easily portable, reliable and sturdy 2. CPAP generator: Option of pressure setting from 3 to 12 cm H2O Should have a detachable overflow container Should deliver the intended pressure constantly and accurately Easy to clean/sterilize The gradations (on the sliding rod) should be easily visible from distance of 6 feet. 3. Air Oxygen Blender Fi0 2 concentration should be adjustable (21-100%) and accurate 4. Humidifier Should automatically regulate the required temperature Should be a closed system for filling up water Should have ports for heater wire as well as temperature probe Should display the chamber temperature and temperature at the patient end. 5. Patient circuits Should have the option of using both disposal and reusable circuits Disposal circuits should be readily available and reasonably priced. Should be able to accommodate a heater wire: heat loss should be minimal along its length. 6. Battery back up Should have a battery back-up for at least 45-60 min. 7. Safety Features Limiting the delivered pressure in the event of an occlusion 8. Device is produced by ISO 9001 certified manufacturer 9. Device is safety certified according CE93/42 FDA 510k or equivalentSupplied with: -5 reusable / disposal to be included. Soft, Pliable nasal prongs-in at least 3 sizes (15 each) |
| 05 | Cardiac monitor/Patient Monitor Quantity: 441 | Multi Parameter Patient Monitor (CE and FDA approved) (ECG, SpO2, NIBP, TEMP, HR/PR, IBP, ETCO2 and CO) Display for easy Viewing 12” or better color TFT/LCD/ LED for easy set. PERFORMANCE Heart rate SPO2 Temperature NIBP IBP ETCO2 CO (Cardiac output) Display: 12” or better touch/button Alarm: Alarm: All parameters on/off selective independently Power input 220Vac,50Hz With Battery Backup ACCESSORIES Wall mounted stand imported Spo2 probe with sensor without extension for adult and paeds NIBP Cuff tube less with hose line for adult and paeds 5 Lead ECG lead Temp probe 2 no’s IBP cable with transducers ETCO2 cable with transducers CO cable with transducers One extra spo2 probe with sensor (Complete without extension) and Nibp cuff with hose line with each unit (Mandatory) All standard accessories Note: The spo2 probe must be without extension One NIBP Simulator, one Spo2 Simulator/analyzer with 50 units (Mandatory) |
| 06 | Blood Gas Analyzer Quantity: 100 | Portable Blood Gas analyzer Sample Volume: 125uL or better Sample Type: Whole Blood, Plasma or Serum Measured Parameters: pH, pO2, pCO2, Na, Cl, K,Ca, Hct. Analysis Time: upto 2min/Sample Up to 5000 patient data storage. With Battery Backup Should be supplied with 200 Tests each parameter |
| 07 | Portable Ultrasound Quantity: 07 | High performance ultrasound scanner System integrates scanner, 2 probes, matching trolley, and video-printer Compact and lightweight, easy to transport and position Alphanumeric keyboard with trackball and time gain control (TCG) Piezoelectric probes, electronically scanned: convex and linear Imaging display modes: B, dual B, M, B and M Adjustable field-of-view 6 level zoom Imaging technologies: dynamic frequency imaging, multi-stage focusing, aperture control Depth range selection: convex sector image and linear image, 3 steps Image orientation: lateral and vertical inversion (in B mode) Freeze function with storage of approx. 25 images Measurements and analysis Calibre control: trackball B-mode image: distance, area and circumference by ellipse and trace method, volume, ratio, gestational age, foetal weight, angle Gestational table: user programmable M-mode: velocity, time interval, depth, heart rate, LV function Alpha-numerics& graphics: Text annotations and body markers Automatic display of date and time, focal point setting, image orientation indicator, image scrolled position, distance scale mark, M-mode time mark, grey scale for calibration High resolution B/W monitor, approx. 25 cm diagonal (across), equals to 10 inch, fit with reflection filter Image grey scale: 256 levels Two transducer ports leave 2 probes permanently available, electronic switch between probes Data communication interface: RS232, BNC, IEEE, USB or equivalent Power supply: 220 V / 50 Hz Convex Abdominal Probe, Frequency range: 2.5/3.5/5.0 MHz Linear Probe, Frequency range: 5.0 to 10.0 MHz |
| 08 | Defibrillator Quantity: 24 | Semi-automatic 270 joules or better biphasic defibrillator with monitor and AED mode. Synchronized output with ECG. Control of energy charging/ delivering on main panel and paddle. The energy range should be adjustable for Peads and adults up to 270 Joules. Charging Time for full energy will be less than 08 sec.or better Screen Size of approx. 6 inch or better colored. Display of Heart Rate: 30 to 300 bpm ECG through Pads / paddles and 3 Lead ECG patient cable with arrhythmia detection Built in recorder for printing of full summery on standard paper including waveforms, Frozen Waveforms, Event Summary, Tabular Trends, User test, and Configuration. Alarms for High and low Heart rate, low battery warning. AC 220V / 50 Hz operated. Built-in Rechargeable battery with charger Auto tester/self-check. External pediatric and adults Paddles, ECG cable with reusable electrodes for adult &Peads. AED facility. AED pads Pacing facility One set of Internal paddles with 10 units (Mandatory) The system must be CE and FDA approved |
| 09 | ECG Machine 3 channels Quantity: 11 | 03 channels ECG Machine with trolly Should be portable and lightweight ADC:12bits, resolution:1uV/LSB Voltage 220 volts, 50hz Display 3” or more Simultaneous 12 leads acquisition Must have continuous display of patient heart and rate Must have integrated pediatric analysis. Support the 12-lead ECG analysis program for complete ECG Analysis reports with measurement data table should be provided. Must be able to indicate at least four critical values that require immediate clinical attention. Printer: High Resolution and in-built thermal array printer. Battery Capacity: Must be 4 hours without printing. Internal memory for storage of patient ECG record. Complete with Patient Cable. Reusable Electrodes Set. The system must be CE and FDA approved One extra ECG lead set with each unit (Mandatory) |
| 10 | Nebulizer Quantity: 20 | Maximum compressor pressure 2.5-3.0 bar Nebulization rate 0.3 ml / min Nebulizer cup capacity 6ml Noise level 55 db or better Electrical requirement 220v/ 50Hz Operation cycles operation for 60min & off for 10min Nebulizer assembly with all Accessories |
| 11 | Suction machine Heavy Duty vertical/ Electric suction Machine vertical Quantity: 29 | Mobile suction pump Oil-Less along with 4 anti- static wheels with lock. Convenient for operation, with following performance features: Built-in Vacuum gauge with a range from: 0-680 mm Hg or better adjustable. The unit must be vertically stand Flow capacity: Not less than 60 l/min or better Explosion proof footswitch. Capacity of two graduated suction bottle: 5L Reusable Vacuum Jar (Autoclavable) Heat resistant and disinfect able silicon tube for suction. Over flow safety device. Sterilizable jars at 121 C Power requirement: 220V, 50Hz. Complete with suction nozzle and other standard accessories. |
| 12 | Oxygen Concentrator Quantity: 75 | Micro Processor controlled. Oxygen Flow Range: 15 litter per Minute or better (Adjustable) With filter. Alarm at very low oxygen level. Audio visual alarm for: Power loss, Low pressure, air leak, hardware failure, Mechanical Failure, Overheating and High Pressure. Oxygen Percentage level: 93%±3% or better With Humidifier With Reusable mask Sizes: 0,1,2,3,4,5 With Connecting Pipe Mobile on 04 Castors |